## Slide 1: The need for AMS assertions
Verify the analog/digital interfaces at block and SoC levels
  Check properties involving voltages and currents
  Check complex timing constraints that don’t fall on digital clock boundaries
Verify analog IP and their correspondence with behavioral models
  Check functional properties of analog IP which involve voltages, currents, and continuous time
AMS assertions will bring similar advantages to AMS verification as SVAs have brought to digital verification
  AMS assertions need to address AMS specific requirements (e.g., continuous time, real valued signals, etc.)

## Slide 2: Examples of assertions
Comparison of voltage and current values:
  If a is greater than 4.5 V then b and c differ by at most 0.1 V.
Timing checks:
  The delay between the crossing of a at 2.5 V and the next crossing of b at 4.5 V is 250.0 ns with a tolerance of 2.5 ns.
Digital to analog interactions:
  If a crosses 0.5 then b should rise followed by c rising 1 clock cycle later.

## Slide 3: ASVA committee vision and status
General vision for ASVA:
  Extend SVA to continuous time while preserving the underlying digital semantics
  Enable SVA expressions to reference real valued signals (e.g., voltages, currents) and events involving them
  Enable assertions to observe relevant quantities from mixed models and eventually integrated SV-VAMS models
  Understand performance/accuracy trade-offs for evaluating assertions with and without influencing the analog solver
Status
  Requirements have been voted upon
  Technical details of implementing the requirements are being investigated
    Relationships with academic temporal logics and the implications for expressiveness and complexity are being considered (e.g., MITL, STL)

## Slide 4: What do we want from P1800?
Feedback from SV-AC (participation is welcome)
Assistance in implementing ASVA requirements, in particular those involving mixed model access, in a way that is harmonious with SV and its roadmap
  A spectrum of solutions has been discussed
  Feasibility of various solutions depends on the progress of the SV-VAMS integration
  Preliminary and interim solutions can be improved with tighter and earlier integration

## Slide 5: Backup slides

## Slide 6: The Analog Engine (A first approximation)
An analog model is fundamentally a set of differential algebraic equations.
  The solution is a function of time.
An analog engine calculates an approximation to the function at a sequence of discrete points in time
  The calculation of each point is computationally costly
The analog engine itself chooses the times
  The engine uses a variety of analytical and heuristic techniques to fine tune the trade-off between accuracy and performance by choosing the time step wisely.
Notes: WE BEGIN with a 30 second lesson in how an analog simulator works.
An analog model is fundamentally a set of differential algebraic equations. The solution is a function of time.
  All the rest is just syntax – Spice, or the AMS languages
A TIME DOMAIN analog engine calculates an approximation to points on the function spaced at a sequence of discrete times.
  The function value is vector consisting of all the currents and voltages of the circuit
The calculation of each point is computationally costly.
The analog engine itself choose the times.
  The user is given some level of control as well through parameters supplied in a control file.
The engine uses a variety of analytical and heuristic techniques to fine tune the trade-off between accuracy and performance by choosing the time step wisely
  `

## Slide 7: The Analog Engine (II) (The Truth)
  That was an over simplification. In truth:
    The user’s model divides time into intervals bounded by the zero crossings of some function of the solution
    Freedom to choose is granted to the engine only in the interior of each interval
  For a complete mixed-signal simulator
    external events from a digital event-driven engine as well as zero crossings can determine the limits of intervals
    The analog engine generates digital events synchronously at zero crossings
  Now, that’s the truth!
Notes:   This is an over-simplification. The truth:
    The user’s model divides time into intervals bounded by the zero crossings of some function of the solution vector
      The function is often something as simple as the difference of two values – in other words, two voltages becoming equal
      The user’s model may modify the equations at the beginning of an interval
    Freedom to choose is granted only in the interior of each interval
      A solution point is calculated at each end of an interval
      (The solution has continuous derivatives wrt time over the interval).
  A second extension creates a mixed-signal simulator
    external events from a digital event-driven engine as well as zero crossings determine the limits of intervals
        Merely sampling the function at some time T requires an estimate of the function at T
      These are D to A events
    The analog engine generates digital events synchronously at zero crossings.
      These are A to D events.
  Now, that’s the truth!

## Slide 8: Assertion requirements
ASVA will include as a subset all productions of the SystemVerilog Assertion language (SVA).
The SVA subset of ASVA will have the same semantics as defined by SystemVerilog.
ASVA will support assertions that refer explicitly to the relative timing of events (temporal distance).
ASVA will support Boolean-valued relational operators on real-valued subexpressions.

## Slide 9: Synchronization requirements
The ability to force an analog solve point from within SystemVerilog.
Access to the double precision time value and analog quantities from the most recent analog solve point.
Ability to read Verilog-AMS quantities from SystemVerilog. The Verilog-AMS value that is read will be equivalent to the value that would be given to a digital request in Verilog-AMS.

## Slide 10: Mixed model access requirements en route to integrated SV-VAMS
Well-defined syntax and semantics for cross instantiation, including the SystemVerilog bind statement
Ability to instantiate a SystemVerilog module or checker within a Verilog-AMS context in a place where a Verilog-AMS module may be instantiated. Ability to bind a SystemVerilog module or checker to a Verilog-AMS target module or modules
Ability to access analog events within SystemVerilog
Ability to assign a real array to a wreal vector

## Slide 11: Mixed model access requirements en route to integrated SV-VAMS
Ability to make SystemVerilog/Verilog-AMS port connections between data types whose connection is legal within SystemVerilog, unless specifically prohibited prior to SV-VAMS integration
  Connect a Verilog-AMS event expression to a checker port of type event
  Connect a Verilog-AMS expression of an integral type to an assignment compatible port as specified in SystemVerilog
  Connect a Verilog-AMS expression of a real or wreal type to a port of a SystemVerilog real type
  Connect a Verilog-AMS expression of type array of real or array of wreal to a port whose type is an unpacked array of SystemVerilog real type